## Slide 1: Road salt: A likely driver of long-term benthic macroinvertebrate decline in an urbanizing stream
Nguyen Tien Anh Quach
August 2nd, 2023
Maryland Department of the Environment
Notes: Road salt: A likely driver of benthic macroinvertebrate decline in urbanizing stream

## Slide 2: Outline
Background Information
Initial phase of rapid urban development
Continuing phase of urbanization
Conclusion

## Slide 3
Urban areas continue to expand
USA
  89% of population by 20501
  3.6% - 8.6% increase in urban land cover by 20602
1UM CSS, 2021; 2Nowak & Greenfield, 2018
Owings Mills, Maryland
Notes: Maryland urbanization?

## Slide 4
Urban areas continue to expand
USA
  89% of population by 20501
  3.6% - 8.6% increase in urban land cover by 20602
Baltimore-DC region
  Consistent growth from 1984 to 2010
  Approx. 11 km2 of new impervious surfaces per year3
1UM CSS, 2021; 2Nowak & Greenfield, 2018; 3Sexton et al., 2013
Sexton et al., 2013
Notes: Maryland urbanization?

## Slide 5
Urban sprawl & the Chesapeake Bay “Pollution Diet”
Consumes large areas of land
Increases reliance on cars
Creates fragmented open spaces
Runoff
  Sediment
  Nutrients
Notes: https://www.cbf.org/issues/land-use/the-impact-of-sprawl.html
What is urban sprawl and why is it bad?
Urban sprawl is a form of unplanned urban and suburban development that takes place over a large area and creates a low-density environment with a high segregation between residential and commercial areas with harmful impacts on the people living in these areas.

## Slide 6
Smart growth as a way to counter urban sprawl
The Avenue at White Marsh
Preserves natural lands
Reduces car dependency and road miles
Better for the Bay?
Notes: South central PA; between 2000 and 2030;

## Slide 7
1984: County Council adopted the Master Plan1
  Owings Mills Town Center
  How to control stormwater runoff?
    Sediment
    Nutrients
1990s-2000s: Rapid urban development
Urban development in Baltimore County
1Baltimore County DPW and DEPRM , 1990
Notes: Tell a story!
Red Run dam
Owings Mills cluster development: https://www.baltimorecountymd.gov/departments/economicdev/meet-baltimore-county/business-communities/owingsmills.html
  The county was trying to manage growth by creating two town centers, including Owings Mills
  Construct a regional flood control/stormwater management facility in RR watershed, where growth will occur
=> Basis for 1990 bioassessment

## Slide 8
Benthic macroinvertebrates
Abundant, easily sampled
Great indicators of localized conditions => early warning!
Broad range of functional feeding groups and tolerance levels to stressors
Credit: Greg Pond, EPA Region 3

## Slide 9: Outline
Background Information
Initial phase of rapid urban development
Continuing phase of urbanization
Conclusion

## Slide 10
How did (a) land cover and (b) water chemistry change over the period 1987-2009?
How did benthic macroinvertebrate communities respond to rapid urban development?
What was the likely cause of benthic decline?
Research questions

## Slide 11
Maryland
Notes: Image of MD and RR showing benthic and water quality sampling sites
1990 Report finding about brook trout.
2009 Repeated Sampling: Hess
Water quality sampling: Same stations.
=> Importance of the study: Before and After; paired design
https://mdewin64.mde.state.md.us/WSA/TierIIWQ/index.html

## Slide 12
Benthic macroinvertebrates
  Hess sampler
  Four times a year (1987-1988 & 2009)
  Data recorded as density per m2
Water chemistry
  Roughly monthly
    n1987 = 11; n2009 = 10 -12
Sampling design
Credit: Danelle Haake
Notes: Image of MD and RR showing benthic and water quality sampling sites
1990 Report finding about brook trout.
2009 Repeated Sampling: Hess
Water quality sampling: Same stations.
=> Importance of the study: Before and After; paired design

## Slide 13
Results

## Slide 14
How did (a) land cover and (b) water chemistry change over the period 1987-2009?
How did benthic macroinvertebrate communities respond to rapid urban development?
What was the likely cause of benthic decline?
Research questions

## Slide 15: 1a. Increase in % developed land varied greatly among the four sub-watersheds.

## Slide 16
Lowest developed land
Highest developed land

## Slide 17: 1b. Increases in specific conductance (SC) in sub-watersheds with high % ISA.
Lowest developed land
Highest developed land

## Slide 18: 1b. Increases in specific conductance (SC) in sub-watersheds with high % ISA.
Lowest developed land
Highest developed land

## Slide 19
How did (a) land cover and (b) water chemistry change over the period 1987-2009?
How did benthic macroinvertebrate communities respond to rapid urban development?
What was the likely cause of benthic decline?
Research questions

## Slide 20
1987-1988 assemblages
2009 assemblages
Early development
Late development
1987-1988
2009
NMDS ordination of relative abundance of benthic taxa

## Slide 21: 2. Benthic communities in 1987-1988 were distinct from those sampled in 2009.
Early development
Late development
1987-1988
2009

## Slide 22
Early development
Late development
1987-1988
2009
NMDS ordination of relative
abundance of benthic taxa
with an overlay
of taxa scores

## Slide 23
Southerland et al., 2005
Maccaffertium (Ephemeroptera:Heptageniidae)
3
BugGuide.Net
Tolerance value 3/10
Sensitive
Notes: TV: expert observation/opinions;

## Slide 24
Tolerance value 3/10
Southerland et al., 2005
Hydropsyche (Trichoptera:Hydropsychidae)
7.5
Sensitive
Macroinvertebrates.org
Tolerance value 3/10
Tolerant
Maccaffertium (Ephemeroptera:Heptageniidae)
3
BugGuide.Net
Notes: Hypotheses:
  Null hypothesis: Taxa were lost totally due to random chance.
  A priori/alternative hypothesis: Based on changes in land cover and water chemistry, urban intolerant taxa were lost.
Tool used: Randomization test
Test statistic: Mean tolerance value of lost taxa
Results: At B1, B2, and B7, null hypothesis rejected.

## Slide 25: 2. Benthic communities in 1987-1988 contained more sensitive taxa than those sampled in 2009.
Early development
Late development
(S) : sensitive taxa
(T) : tolerant taxa
6S & 2T
3S & 5T
1987-1988
2009

## Slide 26
(S) : sensitive taxa
(T) : tolerant taxa
Early development
Late development
Chironomidae
  At B2: 47% 25%

## Slide 27
(S) : sensitive taxa
(T) : tolerant taxa
Early development
Late development
Chironomidae
  At B2: 47% 25%
Oligochaeta
  At B10: 62% 6%

## Slide 28: 2. Relative abundances of Chironomidae , Oligochaeta , and Hydropsychidae .
(S) : sensitive taxa
(T) : tolerant taxa
Early development
Late development
Chironomidae
  At B2: 47% 25%
Oligochaeta
  At B10: 62% 6%
Hydropsychidae
  In 1987-1988: 1-7%
  In 2009: 13-50%

## Slide 29
How did (a) land cover and (b) water chemistry change over the period 1987-2009?
How did benthic macroinvertebrate communities respond to rapid urban development?
What was the likely cause of benthic decline?
Research questions

## Slide 30
At which 95% of a benthic genus is extirpated
Developed for Northern Piedmont of Maryland1
Cormier et al., 2018
XC95 (extirpation level of specific conductance)
351 S/cm
1518 S/cm
Notes: Hypotheses:
  Null hypothesis: Taxa were lost totally due to random chance.
  A priori/alternative hypothesis: Based on changes in land cover and water chemistry, urban intolerant taxa were lost.
Tool used: Randomization test
Test statistic: Mean tolerance value of lost taxa
Results: At B1, B2, and B7, null hypothesis rejected.

## Slide 31
Notes: Hypotheses:
  Null hypothesis: Taxa were lost totally due to random chance.
  A priori/alternative hypothesis: Based on changes in land cover and water chemistry, urban intolerant taxa were lost.
Tool used: Randomization test
Test statistic: Mean tolerance value of lost taxa
Results: At B1, B2, and B7, null hypothesis rejected.

## Slide 32
Notes: Hypotheses:
  Null hypothesis: Taxa were lost totally due to random chance.
  A priori/alternative hypothesis: Based on changes in land cover and water chemistry, urban intolerant taxa were lost.
Tool used: Randomization test
Test statistic: Mean tolerance value of lost taxa
Results: At B1, B2, and B7, null hypothesis rejected.

## Slide 33
Notes: Hypotheses:
  Null hypothesis: Taxa were lost totally due to random chance.
  A priori/alternative hypothesis: Based on changes in land cover and water chemistry, urban intolerant taxa were lost.
Tool used: Randomization test
Test statistic: Mean tolerance value of lost taxa
Results: At B1, B2, and B7, null hypothesis rejected.

## Slide 34
Notes: Hypotheses:
  Null hypothesis: Taxa were lost totally due to random chance.
  A priori/alternative hypothesis: Based on changes in land cover and water chemistry, urban intolerant taxa were lost.
Tool used: Randomization test
Test statistic: Mean tolerance value of lost taxa
Results: At B1, B2, and B7, null hypothesis rejected.

## Slide 35
Most lost genera have XC95 less than 1000 S/cm
3. Significant loss of salt-sensitive genera occurred at downstream mainstem stations.
Notes: Hypotheses:
  Null hypothesis: Taxa were lost totally due to random chance.
  A priori/alternative hypothesis: Based on changes in land cover and water chemistry, urban intolerant taxa were lost.
Tool used: Randomization test
Test statistic: Mean tolerance value of lost taxa
Results: At B1, B2, and B7, null hypothesis rejected.

## Slide 36
*
*
*
Most lost genera have XC95 less than 1000 S/cm
*
*
p < 0.05
3. Significant loss of salt-sensitive genera occurred at downstream mainstem stations.
Notes: Hypotheses:
  Null hypothesis: Taxa were lost totally due to random chance.
  A priori/alternative hypothesis: Based on changes in land cover and water chemistry, urban intolerant taxa were lost.
Tool used: Randomization test
Test statistic: Mean tolerance value of lost taxa
Results: At B1, B2, and B7, null hypothesis rejected.

## Slide 37
*
*
*
Most lost genera have XC95 less than 1000 S/cm
*
*
Maximum SC recorded in 2009
Estimated maximum SC
*
*
*
*
*
3. Significant loss of salt-sensitive genera occurred at downstream mainstem stations.
Notes: Hypotheses:
  Null hypothesis: Taxa were lost totally due to random chance.
  A priori/alternative hypothesis: Based on changes in land cover and water chemistry, urban intolerant taxa were lost.
Tool used: Randomization test
Test statistic: Mean tolerance value of lost taxa
Results: At B1, B2, and B7, null hypothesis rejected.

## Slide 38
*
*
*
Most lost genera have XC95 less than 1000 S/cm
*
*
Maximum SC recorded in 2009
Estimated maximum SC
*
*
*
*
*
3. Significant loss of salt-sensitive genera occurred at downstream mainstem stations.
Notes: Hypotheses:
  Null hypothesis: Taxa were lost totally due to random chance.
  A priori/alternative hypothesis: Based on changes in land cover and water chemistry, urban intolerant taxa were lost.
Tool used: Randomization test
Test statistic: Mean tolerance value of lost taxa
Results: At B1, B2, and B7, null hypothesis rejected.

## Slide 39
Strong relationship between road density and Na+, Cl-, and conductivity1
From 2001 to 2021
  Per year in Baltimore County2
    More than 8 million dollars
    Nearly 61,000 tons of salt
Image from https://www.wbaltv.com/article/salt-brine-used-to-treat-roads-can-damage-your-car/7092181
Roadways De-icing salt application
1A. M. Wallace et al., 2013; 2https://www.baltimorecountymd.gov/departments/public-works/highways/index.html
Notes: 12oz mug = 10 sidewalk squares
Training and Education
MDE is working on certification programs for winter salt applicators and property owners. The programs will focus on how to keep roads safe while reducing impacts to the environment.

## Slide 40
Salt application impairs freshwater ecosystems
Subcategory 5s
Maryland Department of the Environment
Notes: ubcategory 5s: Waterbody impairment is caused by chloride from road salt. Waters assessed in Category 5s are high priority to be addressed through pollution control requirements and restoration approaches, and lower priority for TMDL development.

## Slide 41
Salt problem still needs to be addressed
Subcategory 5s
Monahan and Stover, 2018
Monahan, 2022
Notes: ubcategory 5s: Waterbody impairment is caused by chloride from road salt. Waters assessed in Category 5s are high priority to be addressed through pollution control requirements and restoration approaches, and lower priority for TMDL development.

## Slide 42
Salt application leads to changes
in water chemistry in urban streams

## Slide 43
Salt application leads to changes
in water chemistry in urban streams
Elevated concentrations of ions and specific conductance (SC)
  In urban streams in the Maryland Piedmont1
  In suburban and urban streams in the Baltimore Metropolitan Area2
    Cl- peaked at 5 g/L
    Remained elevated throughout the year
1Moore et al., 2017; 2Kaushal et al., 2005
Notes: 25% sea water; 100 times greater than conc in forested and agricultural streams

## Slide 44
Salt application leads to changes
in water chemistry in urban streams
1Moore et al., 2017; 2Kaushal et al., 2005; 3Moore et al., 2020
Mill Creek, VA
Paint Branch, MD
Sligo Creek, MD
Notes: Meanwhile, the concentrations frequently exceeded the chronic (230 mg/L) and acute (860 mg/L) exposure limit by the U.S. Environmental Protection Agency (US EPA, 1988) in Paint Branch (13.4% ISA) and Sligo Creek (27.1% ISA), Maryland (Moore et al., 2020).

## Slide 45
Salt application leads to changes
in water chemistry in urban streams
1Moore et al., 2017; 2Kaushal et al., 2005; 3Moore et al., 2020
Mill Creek, VA
Paint Branch, MD
Sligo Creek, MD
Notes: Meanwhile, the concentrations frequently exceeded the chronic (230 mg/L) and acute (860 mg/L) exposure limit by the U.S. Environmental Protection Agency (US EPA, 1988) in Paint Branch (13.4% ISA) and Sligo Creek (27.1% ISA), Maryland (Moore et al., 2020).

## Slide 46
Salt application leads to changes
in water chemistry in urban streams
1Moore et al., 2017; 2Kaushal et al., 2005; 3Moore et al., 2020
Mill Creek, VA
Paint Branch, MD
Sligo Creek, MD
Notes: Meanwhile, the concentrations frequently exceeded the chronic (230 mg/L) and acute (860 mg/L) exposure limit by the U.S. Environmental Protection Agency (US EPA, 1988) in Paint Branch (13.4% ISA) and Sligo Creek (27.1% ISA), Maryland (Moore et al., 2020).

## Slide 47
Lakes/Ponds
  Zooplankton1
    Density
    Community composition
  Amphibians2
    Survival of eggs and pre-metamorphosed larvae
Streams
  Fish3
  Benthic macroinvertebrates4
1van Meter et al., 2011; 2Bishop et al., 2000; 3Morgan et al., 2012; 4A. M. Wallace & Biastoch, 2016
Increased salinity negatively impacts aquatic organisms

## Slide 48
Summary

## Slide 49
1. How did (a) land cover and (b) water chemistry change over the period 1987-2009?
  Increases in developed land and SC (also Cl- and Ca2+) with great variations among sub-watersheds.
Summary
2. How did benthic macroinvertebrate communities respond to rapid urban development?
Benthic assemblages were distinct between 1987 and 2009.
3. What was the likely cause of benthic decline?
Road salt was likely a driving cause of benthic declines, especially at downstream mainstem stations.

## Slide 50: Outline
Background Information
Initial phase of rapid urban development
Continuing phase of urbanization
Conclusion

## Slide 51
Stormwater management features (SMFs)

## Slide 52
Stormwater management features (SMFs)
Functions
  stormwater velocity
  nutrient & sediment inputs
  Habitats for organisms

## Slide 53
Index of Biotic Integrity1
1Southerland et al., 2005
Quick and cost-effective method
Integrates metrics from species richness, composition, and tolerance to stressors
Maryland
  Coastal Plain; Piedmont; Combined Highlands
BugGuide.Net
Macroinvertebrates.org

## Slide 54
Index of Biotic Integrity1
1Southerland et al., 2005
Quick and cost-effective method
Integrates metrics from species richness, composition, and tolerance to stressors
Maryland
  Coastal Plain; Piedmont; Combined Highlands
    Number of taxa/EPT taxa/Ephemeroptera taxa
    Percent intolerant urban
    Percent Ephemeroptera
    Percent Clinger
    Percent Chironomidae
BugGuide.Net
Macroinvertebrates.org

## Slide 55
How did (a) land cover and (b) water chemistry change over the period 2009-2019?
How did benthic macroinvertebrate communities respond to the continuing phase of urban development?
Research questions

## Slide 56
Benthic macroinvertebrates
  MBSS protocol: D-net
  Once per year at randomly selected sites
  Data recorded as abundance
  Metrics and IBI scores1 calculated
Water chemistry
  Recorded concurrently
Sampling design
1Southerland et al., 2005
Notes: Image of MD and RR showing benthic and water quality sampling sites
1990 Report finding about brook trout.
2009 Repeated Sampling: Hess
Water quality sampling: Same stations.
=> Importance of the study: Before and After; paired design

## Slide 57
How did (a) land cover and (b) water chemistry change over the period 2009-2019?
How did benthic macroinvertebrate communities respond to the chronic state of urban development?
Research questions

## Slide 58: 1a. Percent developed land stabilized1 in two sub-watersheds and slightly increased in the other two.
1Bird et al., 2018

## Slide 59: 1a. Percent developed land stabilized1 in two sub-watersheds and slightly increased in the other two.
1Bird et al., 2018

## Slide 60: 1b. SC and ISC had a positive association.

## Slide 61
How did (a) land cover and (b) water chemistry change over the period 2009-2019?
How did benthic macroinvertebrate communities respond to the continuing phase of urban development?
Research questions

## Slide 62
2. Assemblages from reference stations consistently had higher IBI scores.
REF-017, B9, and US-B7
  Good & Fair (3.33 – 4.33)
Other stations
  Very Poor & Poor (1.67 – 2.67)
Important metrics
    Number of EPT taxa/Ephemeroptera taxa
    Percent intolerant urban
    Percent Ephemeroptera

## Slide 63
High development
Low development
Before 2014
After 2014
Reference stations
After 2014
Before 2014
NMDS ordination of IBI scores and metrics
Before 2014
2014
After 2014

## Slide 64: 2. Assemblages from reference stations were distinct from others in urbanized sub-watersheds, which were different between before and after 2014.
High development
Low development
Before 2014
After 2014
Chironomidae
  Consistent with previous period
Clingers
  Hydropsychidae!

## Slide 65: SMFs may not be effective in reducing salt inputs into stream1,2
1Snodgrass et al., 2017; 2Casey et al., 2013

## Slide 66
Summary

## Slide 67
How did (a) land cover and (b) change over the period 2009-2019?
  (a) Two sub-watersheds entered a stable state of land cover, whereas other two slightly increased in developed land.
  (b) SC and ISC had positive association.
Summary
2. How did benthic macroinvertebrate communities respond to the chronic state of urban development?
Benthic assemblages were distinct between reference stations and those in urbanized sub-watersheds, which were different before and after 2014.

## Slide 68: Outline
Background Information
Initial phase of rapid urban development
Continuing phase of urbanization
Conclusion

## Slide 69
De-icing salt application increased SC and major ion concentrations (e.g., Cl-, Ca2+).
Benthic communities in urbanized sub-watersheds differed between (a) 1987-1988 and 2009 and (b) before and after 2014, with great increases in hydropsychid caddisflies.
Road salt resulted in significant losses of salt-sensitive genera.
SMFs may not be effective in reducing the salt inputs into stream.
Conclusion

## Slide 70
QUESTIONS?